## Slide 1: Boone County Mackey Bridge

## Slide 2: Overview
Design by Iowa DOT
  First ABC concept in Iowa
3 span pre-stressed girder
  47’-5, 56’-6, 47’-5 Spans
  151’ long x 33’ wide
Precast substructure and superstructure elements
Winning Bid Total $737,098
Bridge Bid $509,173
Bridge Unit Cost $90/SF
Notes: Panels 8 ft? long (in long. Direction) with 60 deg skew…..

## Slide 3: Substructure
Notes: Integral abutment casts in place…another step on critical path
High early strength concrete mix in blockouts

## Slide 4: Superstructure
32 Interior deck panels
    Each ½ bridge width
4 End panels with PT
anchorage zones
Pretensioned transversely
Post-tensioned longitudinally
Notes: 8 ft 1 by 16 ft 1 and 8 ¼ in deep with female to female transverse joints and diamond plates

## Slide 5
Notes:   Modified LXA beams - spacing 8’-4
Setting Panels
Leveling Panels
Casting Transverse Joints
Post-Tensioning
Casting Longitudinal Joints and Abutment Diaphragms

## Slide 6: Monitoring Program
Evaluate
  Structural performance of precast concrete bridge elements in the laboratory
  Constructability of connections
  Handling of components
Monitor and evaluate structural performance of bridge during and after construction
Notes: Technical part is obj 1
Important nontechnical issue is to request supplemental funding to produce a better product from work research already initiated and funded by others

## Slide 7: Laboratory Tests