## Slide 1
Transportation Commission Workshop
February 9, 2021

## Slide 2
Pavement Management
Chris Brakke, PE
Iowa DOT Construction and Materials Bureau

## Slide 3: Pavement system components
Pavement
  Concrete (rigid), Asphalt (flexible), or Composite
Subbase
  Rock layer for support and drainage
Subgrade
  Improved soil layer to provide support
Pavement
Subbase
Subgrade

## Slide 4: Pavement system components
Pavement design life is 40 years.
  Can be extended with proper maintenance and rehabilitation, but not indefinitely.
Many factors influence the design
  Truck traffic
  Subgrade soil
  Climate

## Slide 5: Pavement Inventory
The Primary system includes 24,534 lane miles of pavement.
  3,848 or about 16% on the Interstate
  758 lane miles of ramps
  Our Investment
    If we had to replace the pavement on all of these roads today, the cost would exceed $21.3 billion.
Notes: These mileages are based on the LRS data, not PMIS.

## Slide 6: Pavement Inventory
Chart: Lane Miles by Decade of Original Construction
| Before 1930 | 1930's | 1940's | 1950's | 1960's | 1970's | 1980's | 1990's | 2000's | 2010's
0 | 20.52 | 22.39 | 9.85 | 276.95 | 377.04 | 504.88 | 778.97 | 1930.84 | 2008.76 | 1418.55
1 | 280.76 | 1436.95 | 491.13 | 1472.36 | 1099.6 | 1419.37 | 840.29 | 582.09 | 114.79 | 94.86
2 | 201.61 | 692.77 | 560.19 | 809.66 | 823.7 | 750.3 | 96.63 | 62.8
3 | 499.62 | 1216.51 | 163.69 | 503.17 | 440.87 | 178.14 | 13.43 | 4.03
4 | 348.75 | 441.34 | 82.55 | 220.93 | 78.56 | 41.03
5 | 108.04 | 106.32 | 12.13 | 17.41 | 26.22
6 | 10.44 | 28.86 | 4.02
 | 1469.74 | 3945.14 | 1319.54 | 3304.5 | 2819.77 | 2919.94 | 1729.32 | 2579.76 | 2123.55 | 1513.41
Notes: This chart includes 23,724 lane miles of mainline pavement on the Primary system (includes Interstates). The median pavement construction year is 1966 (50% were built prior to 1966) based on PMIS 2019. Using 2021 as our starting point, 56.8% of lane miles are at least 50 years old (CONYR = 1971 or older), and 29.9% are more than 70 years old.

## Slide 7: Pavement Inventory
Half of the system’s original pavement is more than 55 years old.
29.9% (7,082 miles) is 70+ years old
Based on the size and age of our system we have a significant financial challenge facing us for the foreseeable future.

## Slide 8: The Challenge
Over the past 30 years we have built or replaced 25% of the system.
Continuing at this rate will mean our pavements need to remain serviceable for 120 years.
To date, we do not have any pavements that have reached that age.....Yet we have already replaced many miles that have not hit that milestone.

## Slide 9: Managing our assets is critical to easing the financial burden
Make efficient investments when managing our pavements.
Use cost effective methods to extend pavement life.

## Slide 10: Pavement Condition
Tracking the condition of pavements on the system is the key
  Pavements deteriorate at different rates and for different reasons
  Knowing the reason helps in making decisions on how to maintain pavements
We assess the condition of all pavements on a periodic basis.
  Key indicators such as roughness and cracking are evaluated at least biennially.
  Other indicators such as friction and structure are also evaluated on a 2 to 5 year cycle.
The condition information as well as details of construction and rehabilitation activities are all tracked in our Pavement Management Information System (PMIS).

## Slide 11: Pavement Condition
Chart: History of Non-Interstate Pavement Condition and 3R Program Expenditures
Expenditures | 70711000 | 83644000 | 90543000 | 221461000 | 83834000 | 137009000 | 172922000 | 172358000 | 170627000 | 145086000 | 112512000 | 89621000 | 93564847.9 | 97000000
% Poor | 1.4 | 1.6 | 2.3 | 2.8 | 2.9 | 4.9 | 4.3 | 4.7 | 4.9 | 4.2 | 3.5 | 2.7 | 2.2 | 2.4
% Fair | 24.5 | 26.9 | 30.6 | 29.9 | 28.6 | 29.2 | 27.1 | 25.5 | 25.3 | 25.6 | 25.5 | 25.3 | 26 | 26.4
% Good | 74.2 | 71.5 | 67.1 | 67.3 | 68.4 | 66 | 68.6 | 69.8 | 69.8 | 70.2 | 71 | 72 | 71.7 | 71.3
Notes: Note that there is a lag in the measurement of condition relative to the investment year. Typically condition lags investment by about three years (highlight how 2009 spike didn’t really show up until 2012).

## Slide 12: Pavement Deterioration
Pavement layers are designed for the anticipated truck loadings and for the environmental conditions
Pavements deteriorate after they are built due to many factors:
  Iowa has one of the harshest environments
    Year long moisture
    Temperature extremes
  Increased truck traffic or heavier trucks
  Subgrade inconsistency
  Drainage issues

## Slide 13: Pavement Deterioration

## Slide 14: Slowing down the deterioration
Reactive Maintenance
  Necessary maintenance but not the best approach
    Patching potholes
    Spot overlays
Preventive Maintenance/Preservation
  Treatments applied to pavements in relatively good condition to extend pavement life and/or improve performance.
  Begin early in pavement life
  Very cost effective
  Treatments may be repeated on a schedule

## Slide 15: Maintaining Good Condition Costs Less
Just like your car or home, routine and preventative maintenance can help extend the life.
  Eventually things wear out and more extensive rehabilitation or replacement is required.
Over the life of a pavement, preservation treatments are like sealing the deck on your house – it can help extend the life, but eventually it will need rehabilitation or replacement.
We use pavement management data and tools to help us determine the optimal mix of treatments to get the most life at the least cost.

## Slide 16: Pavement Treatments
Maintenance/Preservation treatments
  Crack & joint sealing/filling
  Diamond grinding
  Thin surface treatments
    Chip seals
    Slurry seals
    Microsurfacing
    Thin lift asphalt overlays
Rehabilitations
  Functional overlays (to address ride)
  Cold-in-Place recycling
  Structural overlays (asphalt and concrete)
  Rubblization/crack & seat
Reconstruction
  Completely replacing the pavement and sometimes the subgrade
$3,000/mile/year
$9,000/mile/year
$10,000/mile/year
$25,000/mile/year
$35,000/mile/year
Increasing Annualized Cost
Notes: Costs (from TAMP): Maint/Pres Tx $20k - $50k per lane mile; Rehab Tx $220k - $500k per LM; Recon Tx $600k - $750k per LM

## Slide 17: Pavement Management
Which treatment to use depends on the condition of the pavement and the life that is needed. A minimal treatment is not the right choice for every pavement.
The right treatment is cost effective because it has the lowest cost and will perform for the desired timeframe.
Some pavements require a higher cost treatment, but it can still be cost effective because it will provide a longer life or a higher level of performance.
The treatment cost and effectiveness are incorporated into the models used to predict pavement needs into the future.

## Slide 18: Condition Forecast Process
Modeling software predicts the system-wide pavement condition under any given funding scenario.
  Models are developed based on past pavement performance to predict future performance.
  The tool evaluates all viable treatment alternatives for each pavement.
  Optimization is used to select the mix of candidates that maximizes network condition.

## Slide 19
Chart: Pavement Condition Index and Funding Non-Interstate Pavement Modernization Program
| 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Expenditures | 70711000 | 83644000 | 90543000 | 221461000 | 83834000 | 137009000 | 172922000 | 172358000 | 170627000 | 145086000 | 112512000 | 89621000 | 93564847.9 | 96900000 | 148000000
Baseline Budget | 105000000 | 115000000 | 140000000 | 145000000 | 150000000 | 155000000 | 165000000 | 175000000 | 185000000 | 190000000
Added funds | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
PCI | 74.819 | 73.4945 | 71.6669 | 71.404 | 70.9146 | 70.0143 | 71.7575 | 72.2124 | 72.4145 | 72.3998 | 73.0989 | 74.0032 | 74.5477 | 74.4395
Forecast PCI | 74.9979 | 74.8987 | 75.0555 | 74.8453 | 74.6962 | 74.4364 | 74.3097 | 74.4441 | 74.3568 | 74.2254 | 73.9963
Target Condition Index
Notes: This chart shows past expenditures in the 3R program (Non-Interstate Pavement Modernization) and pavement condition. It is important to note there is about a 3-year lag in the condition measurement – projects in FY19 might not be complete until the fall of 2019, and often those won’t be evaluated again for another year or two so we might not see their condition reflected until the 2021 data. This lag is why we see the unexpected relationship between expenditures and condition.

## Slide 20
PCI = 75
PCI = 33
PCI = 50

## Slide 21
Chart: Pavement Condition Index at 125% Funding Scenario Non-Interstate Pavement Modernization Program
| 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Baseline | 148000000 | 105000000 | 115000000 | 140000000 | 145000000 | 150000000 | 155000000 | 165000000 | 175000000 | 185000000 | 190000000 | 195000000
Added funds | 0 | 0 | 0 | 0 | 0 | 0 | 38000000 | 39250000 | 41750000 | 44250000 | 45500000 | 46750000
Forecast PCI | 74.9979 | 74.8987 | 75.0555 | 74.8382 | 74.6861 | 74.439 | 74.3114 | 74.6974 | 74.7349 | 74.7454 | 74.7828 | 74.6044

## Slide 22
Chart: Pavement Condition Index at $20M steps Funding Scenario Non-Interstate Pavement Modernization Program
| 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Baseline | 148000000 | 105000000 | 115000000 | 140000000 | 145000000 | 150000000 | 150000000 | 150000000 | 150000000 | 150000000 | 150000000 | 150000000
Added funds | 0 | 0 | 0 | 0 | 0 | 0 | 20000000 | 40000000 | 60000000 | 80000000 | 100000000 | 120000000
Forecast PCI | 74.9979 | 74.8987 | 75.0555 | 74.8382 | 74.6861 | 74.4391 | 74.3115 | 74.56 | 74.5618 | 74.5461 | 74.607 | 74.5224

## Slide 23
Chart: Pavement Condition Index at 150% Funding Scenario Non-Interstate Pavement Modernization Program
| 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Baseline | 137400000 | 105000000 | 115000000 | 140000000 | 145000000 | 150000000 | 155000000 | 165000000 | 175000000 | 185000000 | 190000000 | 195000000
Added funds | 0 | 0 | 0 | 0 | 0 | 0 | 75000000 | 78500000 | 83500000 | 88500000 | 91000000 | 93500000
Forecast PCI | 74.9979 | 74.8987 | 75.0555 | 74.8382 | 74.6861 | 74.4391 | 74.3115 | 74.9206 | 75.1192 | 75.3408 | 75.3186 | 75.6495

## Slide 24
Chart: Non-Interstate Pavement Modernization Budget Scenario Comparison
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031
75% Current Funding | 74.9979 | 74.8987 | 75.0555 | 74.8382 | 74.6861 | 74.4391 | 74.3115 | 74.132 | 73.9468 | 73.6465 | 73.3388 | 72.9853
100% Current Funding | 74.9979 | 74.8987 | 75.0555 | 74.8453 | 74.6962 | 74.4364 | 74.3097 | 74.4441 | 74.3568 | 74.2254 | 73.9963 | 73.9157
125% Current Funding | 74.9979 | 74.8987 | 75.0555 | 74.8382 | 74.6861 | 74.439 | 74.3114 | 74.6974 | 74.7349 | 74.7454 | 74.7828 | 74.6044
150% Current Funding | 74.9979 | 74.8987 | 75.0555 | 74.8382 | 74.6861 | 74.4391 | 74.3115 | 74.9206 | 75.1192 | 75.3408 | 75.3186 | 75.6495
175% Current Funding | 74.9979 | 74.8987 | 75.0555 | 74.8453 | 74.6962 | 74.4334 | 74.3068 | 75.1129 | 75.4664 | 75.7866 | 76.1753 | 76.6837

## Slide 25: Key Take-aways
Continuing at recent levels of funding for pavement reconstruction will require our pavements to last 120 years.
Recent funding increases have helped reduce the decline of the system.
While short term funding can meet our target condition, long term needs are out-pacing our level of investment in pavement reconstruction.
The reason is that Iowa’s highway system has been built over the past 100 years to the size it is today. At this point, current projected funding is not adequate to sustain a system of this size in a state of good repair.