## Slide 1
Transportation Commission Workshop
January 8, 2019

## Slide 2
Transportation Asset Management
Charlie Purcell, PE
Iowa DOT Project Delivery Bureau

## Slide 3: Information to Inform Decisions
Dec-2018 - Bridge Management
Jan-2019 - Pavement Management
Feb-2019 - Interstate System Planning
Mar-2019 - Investment Alternatives
Apr-2019 - Mobility Strategies (ICM)
May-2019 - Draft Program Asset Management Summary

## Slide 4
Pavement Management
Chris Brakke, PE
Iowa DOT Office of Construction and Materials

## Slide 5: Pavement system components
Pavement
  Concrete (rigid), Asphalt (flexible), or Composite
Subbase
  Rock layer for support and drainage
Subgrade
  Improved soil layer to provide support
Pavement
Subbase
Subgrade

## Slide 6: Pavement Inventory
The primary system includes 24,502 lane miles of pavement.
  3,820 or about 16% on the Interstate
  754 lane miles of ramps
If we had to replace the pavement on all of these roads today, the cost would exceed $14.2 billion.

## Slide 7: Pavement Inventory
Chart: Lane Miles by Decade of Original Construction
| Before 1930 | 1930's | 1940's | 1950's | 1960's | 1970's | 1980's | 1990's | 2000's | 2010's
0 | 3.39 | 45.18 | 12.2 | 305.38 | 367.39 | 562.07 | 880.1 | 2150.33 | 2021.1 | 1080.22
1 | 70.23 | 474.92 | 353.41 | 1027.73 | 1016.21 | 1526.5 | 811.06 | 406.64 | 50.83 | 19.09
2 | 262.97 | 1164.72 | 636.5 | 1302.35 | 1002.01 | 817.37 | 66.45 | 25.91 | 0 | 0
3 | 764.8 | 1647.28 | 251.2 | 560.99 | 415.28 | 65.51 | 0 | 0 | 0 | 0
4 | 326.3 | 467.87 | 59.87 | 80.14 | 53.52 | 0 | 0 | 0 | 0 | 0
5 | 78.46 | 138.24 | 3.47 | 8.95 | 0 | 0 | 0 | 0 | 0 | 0
6 | 0.66 | 2.46 | 0 | 4.02 | 0 | 0 | 0 | 0 | 0 | 0
 | 1506.81 | 3940.67 | 1316.65 | 3289.56 | 2854.41 | 2971.45 | 1757.61 | 2582.88 | 2071.93 | 1099.31
Notes: This chart includes 23,391 lane miles of mainline pavement on the Primary system (includes Interstates). The median pavement construction year is 1965 (50% were built prior to 1965) based on PMIS 2017. Using 2019 as our starting point, 55.2% of lane miles are at least 50 years old (CONYR = 1969 or older), and 29% are more than 70 years old.

## Slide 8: Pavement Inventory
Pavement design life is 40 years.
  Can be extended with proper maintenance and rehabilitation, but not indefinitely.
Half of the system’s original pavement is more than 55 years old.
29% (6,792 miles) is 70+ years old
If we only build/replace 2,000 miles per decade as we did in the first decade of the 2000’s, we would need original pavements to last at least 110 years.

## Slide 9: Pavement Condition
Tracking the condition of pavements on the system is the key
  Pavements deteriorate at different rates and for different reasons
  Knowing the reason helps in making decisions on how to maintain pavements
We assess the condition of all pavements on a periodic basis.
  Key indicators such as roughness and cracking are evaluated at least biennially.
  Other indicators such as friction and structure are also evaluated on a 2 to 5 year cycle.
The condition information as well as details of construction and rehabilitation activities are all tracked in our Pavement Management Information System (PMIS).

## Slide 10: Pavement Condition
Chart: History of Non-Interstate Pavement Condition and 3R Program Expenditures
Expenditures | 61277000 | 70711000 | 83644000 | 90543000 | 221461000 | 83834000 | 137009000 | 172922000 | 172358000 | 170627000 | 145086000 | 112512000 | 89621000
% Poor | 1.4 | 1.6 | 2 | 2.7 | 2.9 | 3.2 | 4.9 | 4.7 | 5 | 5.2 | 4.2 | 3.7 | 2.8
% Fair | 26 | 25.1 | 27.6 | 31.1 | 30.5 | 29.1 | 29.8 | 27.8 | 28 | 26.9 | 26.4 | 26.1 | 25.5
% Good | 72.6 | 73.3 | 70.4 | 66.2 | 66.5 | 67.6 | 65.3 | 67.6 | 67 | 67.9 | 69.4 | 70.2 | 71.7
Notes: Note that there is a lag in the measurement of condition relative to the investment year. Typically condition lags investment by about three years (highlight how 2009 spike didn’t really show up until 2012).

## Slide 11: Pavement Deterioration
Pavement layers are designed for the anticipated truck loadings and for the environmental conditions
Pavements deteriorate after they are built due to many factors:
  Iowa has one of the harshest environments
    Year long moisture
    Temperature extremes
  Increased truck traffic or heavier trucks
  Subgrade inconsistency
  Drainage issues

## Slide 12: Pavement Deterioration

## Slide 13: Good Roads Cost Less
Just like your car or home, routine and preventative maintenance can help extend the life.
  Eventually things wear out and more extensive rehabilitation or replacement is required.
Over the life of a pavement, preservation treatments are like sealing the deck on your house – it may help extend the life, but eventually it will need rehabilitation or replacement.
We use pavement management data and tools to help us determine the optimal mix of treatments to get the most life at the least cost.

## Slide 14: Pavement Treatments
Maintenance/Preservation treatments
  Crack & joint sealing/filling
  Patching
  Diamond grinding
  Thin surface treatments
    Chip seals
    Slurry seals
    Microsurfacing
    Thin lift asphalt overlays
Rehabilitations
  Functional overlays (to address ride)
  Cold-in-Place recycling
  Structural overlays (asphalt and concrete)
  Rubblization/crack & seat
Reconstruction
  Completely replacing the pavement and sometimes the subgrade
Increasing annualized cost
Notes: Costs (from TAMP): Maint/Pres Tx $20k - $50k per lane mile; Rehab Tx $220k - $500k per LM; Recon Tx $600k - $750k per LM

## Slide 15: Pavement Management
Which treatment to use depends on the condition of the pavement and the life that is needed. A minimal treatment is not the right choice for every pavement.
The right treatment is cost effective because it has the lowest cost and will perform for the desired timeframe.
Some pavements require a higher cost treatment, but it will still be cost effective because it will provide a longer life or a higher level of performance.
The treatment cost and effectiveness are incorporated into the models used to predict pavement needs.

## Slide 16: Condition Forecast Process
Modeling software predicts the system-wide pavement condition under any given funding scenario.
  Models are developed based on past pavement performance to predict future performance.
  The tool evaluates all viable treatment alternatives for each pavement.
  Optimization is used to select the mix of candidates that maximizes network condition.

## Slide 17
Chart: Pavement Condition Index and Funding Non-Interstate Pavement Modernization Program
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Expenditures | 61277000 | 70711000 | 83644000 | 90543000 | 221461000 | 83834000 | 137009000 | 172922000 | 172358000 | 170627000 | 145086000 | 112512000 | 89621000 | 93564847.9 | 95400000
Baseline Budget | 100000000 | 105000000 | 115000000 | 125000000 | 130000000 | 135000000 | 140000000 | 150000000 | 160000000
Added funds | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
PCI | 74.9 | 75.2 | 73.9 | 72 | 71.4 | 71.2 | 70.2 | 71.7 | 70.9 | 71.5 | 72.2 | 72.8 | 74.1
Forecast PCI | 74.2877 | 74.6934 | 72.2082 | 70.7985 | 70.1728 | 69.6175 | 69.1542 | 68.9536 | 68.8144 | 68.7504 | 68.7828 | 68.8446
Target Condition Index
Notes: This chart shows past expenditures in the 3R program (Non-Interstate Pavement Modernization) and pavement condition. It is important to note there is about a 3-year lag in the condition measurement – projects in FY19 might not be complete until the fall of 2019, and often those won’t be evaluated again for another year or two so we might not see their condition reflected until the 2021 data. This lag is why we see the unexpected relationship between expenditures and condition.

## Slide 18
Chart: Pavement Condition Index at 150% Funding Scenario Non-Interstate Pavement Modernization Program
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Baseline | 95400000 | 100000000 | 105000000 | 115000000 | 125000000 | 130000000 | 135000000 | 140000000 | 150000000 | 160000000
Added funds | 0 | 50000000 | 52500000 | 57500000 | 62500000 | 65000000 | 67500000 | 70000000 | 75000000 | 80000000
Forecast PCI | 72.2082 | 70.7985 | 70.6667 | 70.4687 | 70.5008 | 70.7419 | 71.0944 | 71.4914 | 71.9018 | 72.3946

## Slide 19
Chart: Pavement Condition Index at 200% Funding Scenario Non-Interstate Pavement Modernization Program
| 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Baseline | 95400000 | 100000000 | 105000000 | 115000000 | 125000000 | 130000000 | 135000000 | 140000000 | 150000000 | 160000000
Added funds | 0 | 100000000 | 105000000 | 115000000 | 125000000 | 130000000 | 135000000 | 140000000 | 150000000 | 160000000
Forecast PCI | 72.2082 | 70.7985 | 71.0839 | 71.3451 | 71.7732 | 72.402 | 73.1591 | 73.8894 | 74.6394 | 75.4659

## Slide 20
Chart: Non-Interstate Pavement Modernization Budget Scenario Comparison
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028
75% Current Funding | 72.2082 | 70.7985 | 69.9186 | 69.187 | 68.5093 | 68.0686 | 67.7459 | 67.4505 | 67.2523 | 67.0741
100% Current Funding | 72.2082 | 70.7985 | 70.1728 | 69.6175 | 69.1542 | 68.9536 | 68.8144 | 68.7504 | 68.7828 | 68.8446
125% Current Funding | 72.2082 | 70.7985 | 70.4257 | 70.0389 | 69.8526 | 69.8524 | 69.9593 | 70.1746 | 70.4121 | 70.7141
150% Current Funding | 72.2082 | 70.7985 | 70.6667 | 70.4687 | 70.5008 | 70.7419 | 71.0944 | 71.4914 | 71.9018 | 72.3946
175% Current Funding | 72.2082 | 70.7985 | 70.8731 | 70.9044 | 71.1339 | 71.5796 | 72.1657 | 72.7236 | 73.3158 | 73.9777
200% Current Funding | 72.2082 | 70.7985 | 71.0839 | 71.3451 | 71.7732 | 72.402 | 73.1591 | 73.8894 | 74.6394 | 75.4659

## Slide 21: Key Take-aways
Continuing at recent levels of funding for reconstruction will require our pavements to last at least 100 years.
Half of the system’s original pavement is more than 55 years old.
  29% (6,792 miles) is 70+ years old
Iowa’s highway system has been built up over the past 100 years to the size it is today. At this point, current projected funding is not adequate to sustain the system in a state of good repair.