## Slide 1
Transportation Commission Workshop
January 9, 2024

## Slide 2
Pavement Management
Chris Brakke, PE
Iowa DOT Construction and Materials Bureau

## Slide 3: Pavement system components
Pavement
  Concrete (rigid), Asphalt (flexible), or Composite
Subbase
  Rock layer for support and drainage
Subgrade
  Improved soil layer to provide support
Pavement
Subbase
Subgrade

## Slide 4: Pavement system components
Pavement design life is 40 years.
  Serviceable life can be extended with maintenance and rehabilitation, but not indefinitely.
Many factors influence the design….
  Truck traffic
  Subgrade soil
  Climate

## Slide 5: Pavement Inventory
The Primary system includes 24,534 lane miles of pavement.
  3,848 or about 16% on the Interstate
  758 lane miles of ramps
  Our Investment
    If we had to replace the pavement on all of these roads today, the cost would exceed $31 billion.
Notes: These mileages are based on the LRS data, not PMIS.

## Slide 6: Pavement Inventory
Chart: Lane Miles by Decade of Original Construction
| Before 1930 | 1930's | 1940's | 1950's | 1960's | 1970's | 1980's | 1990's | 2000's | 2010's | 2020's
0 | 0.71 | 28.11 | 3.87 | 204.03 | 261.25 | 408.97 | 626.29 | 1879.3 | 1945.26 | 1463.36 | 316.77
1 | 48.3 | 317.84 | 218.9 | 802.83 | 807.1 | 1245.34 | 813.73 | 532.23 | 109.2 | 74.99 | 5.92
2 | 154.54 | 1025.74 | 610.07 | 1195.93 | 1008.09 | 1063.56 | 211.56 | 122.35 | 59.45 | 0 | 0
3 | 645.65 | 1487.32 | 268.48 | 844.9 | 464.78 | 204.65 | 21.94 | 0 | 2.77 | 0 | 0
4 | 479.21 | 792.39 | 168.26 | 174.87 | 177.2 | 0 | 1.86 | 0 | 0 | 0 | 0
5 | 61.44 | 189.65 | 22.8 | 11.1 | 29.07 | 0 | 0 | 0 | 0 | 0 | 0
6 | 10.44 | 68.11 | 0 | 27.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1400.29 | 3909.16 | 1292.38 | 3261.26 | 2747.49 | 2922.52 | 1675.38 | 2533.88 | 2116.68 | 1538.35 | 322.69
Notes: This chart includes 23,723 lane miles of mainline pavement on the Primary system (includes Interstates). The median pavement construction year is 1968 (50% were built prior to 1968) based on PMIS 2022. Using 2022 as our starting point, 58.7% of lane miles are at least 50 years old (CONYR = 1973 or older), and 31.4% are more than 70 years old.

## Slide 7: Pavement Inventory
Half of the system’s original pavement is more than 55 years old.
31% (7,449 miles) is 70+ years old
Based on the size and age of our system we have a significant financial challenge facing us for the foreseeable future.

## Slide 8: The Challenge
We need to be replacing more pavements on our aging system.
An achievable life for a pavement is something less than 100 years (this will include 3-4 overlays).
To date, we only have a few pavements that have reached that age.....Yet we have already replaced many miles that have not hit that milestone.

## Slide 9: The Challenge
Last year $35M was approved for pavement replacements beginning in FY 2027
    Good start to begin addressing needs
A 100 year life requires 1% replacement/year.
    Which equates to roughly $310M/year in additional funding beyond projected 3R funds.
Currently $35M/yr = 0.1% of the system/year
Propose to keep this as a priority and continue to grow additional funding for pavement

## Slide 10: Construction costs for highway projects
2-lane highway (rural)
  New Construction - $ 7.4 million per mile
  Pavement replacement - $3.2 million per mile
  Resurfacing (3”) - $625,000 per mile

## Slide 11: Managing our assets is critical to address this challenge and to ease the financial burden
We need to make efficient investments when managing our pavements.
Use cost effective methods to extend pavement life.

## Slide 12: Pavement Condition
Chart: History of Non-Interstate Pavement Condition and 3R Program Expenditures
Expenditures | 221461000 | 83834000 | 137009000 | 172922000 | 172358000 | 170627000 | 145086000 | 112512000 | 89621000 | 93564848 | 96900000 | 137400000 | 105000000
% Poor | 1.7 | 1.9 | 3 | 2.5 | 3.6 | 3.7 | 3.2 | 2.7 | 2 | 1.6 | 1.8 | 2.3 | 2 | 1.7
% Fair | 30.9 | 29.6 | 31 | 28.8 | 26.5 | 26.4 | 26.5 | 26.3 | 26.1 | 26.6 | 26.9 | 27.7 | 28.7 | 27.6
% Good | 67.3 | 68.4 | 66 | 68.6 | 69.8 | 69.8 | 70.2 | 71 | 72 | 71.7 | 71.3 | 70 | 69.3 | 70.7
Notes: Note that there is a lag in the measurement of condition relative to the investment year. Typically condition lags investment by about three years (highlight how 2009 spike didn’t really show up until 2012).

## Slide 13: Pavement Deterioration
Pavement layers are designed for the anticipated truck loadings and for the environmental conditions
Pavements deteriorate after they are built due to many factors:
  Iowa has one of the harshest environments
    Year long moisture
    Temperature extremes
  Increased truck traffic or heavier trucks
  Subgrade inconsistency
  Drainage issues

## Slide 14: Pavement Deterioration

## Slide 15: Slowing down the deterioration
Preventive Maintenance/Preservation
  Treatments applied to pavements in relatively good condition to extend pavement life and/or improve performance.
  Begin early in pavement life
  Very cost effective
  Treatments may be repeated on a schedule

## Slide 16: Maintaining Good Condition Costs Less
Just like your car or home, routine and preventative maintenance can help extend the life.
  Eventually things wear out and more extensive rehabilitation or replacement is required.
Over the life of a pavement, preservation treatments are like sealing the deck on your house – it can help extend the life, but eventually it will need rehabilitation or replacement.
We use pavement management data and tools to help us determine the optimal mix of treatments to get the most life at the least cost.

## Slide 17: Pavement Treatments
Maintenance/Preservation treatments
  Crack & joint sealing/filling
  Diamond grinding
  Thin surface treatments
    Chip seals
    Slurry seals
    Microsurfacing
    Thin lift asphalt overlays
Rehabilitations (20 year life)
  Functional overlays (to address ride)
  Cold-in-Place recycling
  Structural overlays (asphalt and concrete)
  Rubblization/crack & seat
Reconstruction (40 year life)
  Completely replacing the pavement and sometimes the subgrade
$3,000/mile/year of life
$9,000/mile/year
$12,000/mile/year
$40,000/mile/year
$80,000/mile/year
Increasing Annualized Cost
Notes: Costs (from TAMP): Maint/Pres Tx $20k - $50k per lane mile; Rehab Tx $220k - $500k per LM; Recon Tx $600k - $750k per LM

## Slide 18
Chart: Pavement Condition Index and Funding Non-Interstate Pavement Modernization Program
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Expenditures | 221461000 | 83834000 | 137009000 | 172922000 | 172358000 | 170627000 | 145086000 | 112512000 | 89621000 | 93564848 | 96900000 | 137400000 | 105000000 | 165000000 | 140000000 | 142000000
Baseline Budget | 150000000 | 155000000 | 165000000 | 210000000 | 220000000 | 225000000 | 230000000 | 235000000 | 240000000 | 245000000
Added funds | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
PCI | 71.8 | 71.3 | 70.4 | 72 | 72.5 | 72.5 | 72.6 | 73.4 | 74.3 | 74.9 | 74.8 | 73.6 | 73.6 | 74.38
Forecast PCI | 74.4 | 75.1 | 75.13 | 75.26 | 75.05 | 74.99 | 74.97 | 74.92 | 74.92 | 74.95 | 74.87 | 74.75 | 74.48
Target Condition Index
Notes: This chart shows past expenditures in the 3R program (Non-Interstate Pavement Modernization) and pavement condition. It is important to note there is about a 3-year lag in the condition measurement – projects in FY19 might not be complete until the fall of 2019, and often those won’t be evaluated again for another year or two so we might not see their condition reflected until the 2021 data. This lag is why we see the unexpected relationship between expenditures and condition.

## Slide 19
PCI = 75
PCI = 33
PCI = 50

## Slide 20
Chart: Non-Interstate Pavement Modernization Budget Scenario Comparison
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Baseline | 74.38 | 75.09 | 75.13 | 75.26 | 75.05 | 74.99 | 74.97 | 74.92 | 74.92 | 74.95 | 74.87 | 74.75 | 74.48 | 74.19
CAP 125% | 74.38 | 75.09 | 75.13 | 75.26 | 75.05 | 74.98 | 74.87 | 74.82 | 75.08 | 75.35 | 75.49 | 75.68 | 75.65 | 75.54
CAP 150% | 74.38 | 75.09 | 75.13 | 75.26 | 75.05 | 74.99 | 74.87 | 74.81 | 75.35 | 75.85 | 76.26 | 76.68 | 76.79 | 76.84
CAP 175% | 74.38 | 75.09 | 75.13 | 75.26 | 75.05 | 74.98 | 74.87 | 74.73 | 75.44 | 76.06 | 76.82 | 77.31 | 77.39 | 77.53
CAP 200% | 74.38 | 75.09 | 75.13 | 75.26 | 75.05 | 74.98 | 74.88 | 74.73 | 75.79 | 76.69 | 77.57 | 78.37 | 78.98 | 78.99

## Slide 21
Chart: Pavement Condition Index at 125% Funding Scenario Non-Interstate Pavement Modernization Program
| 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
Baseline | 142000000 | 150000000 | 155000000 | 165000000 | 210000000 | 220000000 | 225000000 | 230000000 | 235000000 | 240000000 | 245000000 | 250000000
Added funds | 0 | 0 | 0 | 0 | 0 | 44250000 | 45500000 | 46750000 | 48000000 | 49250000 | 50500000 | 52000000
Forecast PCI | 75.13 | 75.26 | 75.05 | 74.98 | 74.87 | 74.82 | 75.08 | 75.35 | 75.49 | 75.68 | 75.65 | 75.54

## Slide 22: Key Take-aways
We have 2 competing goals for pavement funding
  Achieve the target 75 PCI condition
  Replace pavements on a reasonable cycle to limit risk of our aging system
While short term funding can meet our target condition, the long-term needs for pavement replacement are out pacing our level of investment…….
    This is because Iowa’s highway system has been built to the current size over the past 100 years. At this point, the projected funding is not adequate to sustain a system of this size in a state of good repair.
Addressing the need for replacing our aged system will eventually require $310M per year (2023 $) in investment to the Primary system to achieve a 100 year replacement cycle.
    This is in addition to the 3R funding already in place.
If additional funding becomes available, use analytics to determine where to direct additional funding between rehabilitation and reconstruction.

## Slide 23: Case history IA 163
Condition in 2006
  Rough ride but pavement in good shape
  1964 PC Concrete
2006

## Slide 24: Case history IA 163
PCC Pavement
Steel Dowel bar
Joint
Truck wheels

## Slide 25: Case history IA 163
PCC Pavement
Joint
Truck wheels

## Slide 26: Decision - preservation/rehab
2007 Dowel bar retrofit & diamond grind

## Slide 27: Decision - preservation/rehab
2007 Dowel bar retrofit & diamond grind
Next rehab is likely an asphalt overlay
2023
2007

## Slide 28: Case history US 34
Condition in 2016
  Cracking and rough ride
  1965 PC Concrete
  1983 asphalt overlay
  1998 asphalt overlay
2016

## Slide 29: Decision - rehabilitate again
2017 Cold-in-place-recycling w/ asphalt overlay
Next time will require major rehabilitation or possibly reconstruction
2023
2017

## Slide 30: Case history IA 14
Condition in 2004
  Cracking and rough ride
  1972 PC Concrete
2004

## Slide 31: Decision – Rehabilitation (2005)
2005 asphalt overlay
2022

## Slide 32: Cores - 2022

## Slide 33: Decision - major rehabilitation
Rubblize existing concrete and place heavy overlay
6.5” thick asphalt overlay
20 year design life with ability to place additional overlays in the future. Similar to new pavement.

## Slide 34: Key Take-aways
We have 2 competing goals for pavement funding
  Achieve the target 75 PCI condition
  Replace pavements on a reasonable cycle to limit risk of our aging system
While short term funding can meet our target condition, the long-term needs for pavement replacement are out pacing our level of investment…….
    This is because Iowa’s highway system has been built to the current size over the past 100 years. At this point, the projected funding is not adequate to sustain a system of this size in a state of good repair.
Addressing the need for replacing our aged system will eventually require $310M per year (2023 $) in investment to the Primary system to achieve a 100 year replacement cycle.
    This is in addition to the 3R funding already in place.
If additional funding becomes available, use analytics to determine where to direct additional funding between rehabilitation and reconstruction.