## Slide 1
Pavement Management
Iowa Transportation Commission Workshop – January 21, 2025
3/2/2023

## Slide 2
Agenda
Pavement Management Team
Pavement Inventory
Pavement Distress and Treatments
Pavement Performance Trends and Budget Scenarios
Strategic Project Selection

## Slide 3
Pavement Management Team Introduction
Ashley Buss, Ph.D., P.E.
Pavement Management Leader
Jason Omundson, P.E.
Pavement Preservation Engineer
Currently hiring
Pavement Modeler and Analyst
Notes: Our team works closely with all the districts, construction and materials, program management, project management, design, research and analytics, and systems planning.

## Slide 4
Guiding Documents
Notes: The Pavement management strategic plan and the programmatic plan are our guiding documents that shaped the vision for creating the team.

## Slide 5
5-year Goals and Objectives
Notes: These goals and objectives link to the Transportation Commission’s State Long-Range Transportation Plan. – particularly the emphasis on stewardship.

## Slide 6
Pavement Inventory
The Primary system includes 24,636 lane miles of pavement.
  3,899 or about 16% on the Interstate
  799 lane miles of ramps
  Our Investment
    If we had to replace the pavement on all of these roads today, the cost would exceed $31 billion.
Notes: One mile of four-lane roadway is four lane-miles.
These mileages are based on the LRS data, not PMIS.
(Documentation: Research & Analytics Bureau report generated 9/26/2024. Provided to me via email on 11/22/2024.)

## Slide 7
Pavement Inventory
Chart: Lane Miles by Decade of Original Construction
| Before 1930 | 1930's | 1940's | 1950's | 1960's | 1970's | 1980's | 1990's | 2000's | 2010's | 2020's
0 | 0.71 | 28.11 | 3.87 | 204.03 | 261.25 | 408.97 | 626.29 | 1879.3 | 1945.26 | 1463.36 | 316.77
1 | 48.3 | 317.84 | 218.9 | 802.83 | 807.1 | 1245.34 | 813.73 | 532.23 | 109.2 | 74.99 | 5.92
2 | 154.54 | 1025.74 | 610.07 | 1195.93 | 1008.09 | 1063.56 | 211.56 | 122.35 | 59.45 | 0 | 0
3 | 645.65 | 1487.32 | 268.48 | 844.9 | 464.78 | 204.65 | 21.94 | 0 | 2.77 | 0 | 0
4 | 479.21 | 792.39 | 168.26 | 174.87 | 177.2 | 0 | 1.86 | 0 | 0 | 0 | 0
5 | 61.44 | 189.65 | 22.8 | 11.1 | 29.07 | 0 | 0 | 0 | 0 | 0 | 0
6 | 10.44 | 68.11 | 0 | 27.6 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1400.29 | 3909.16 | 1292.38 | 3261.26 | 2747.49 | 2922.52 | 1675.38 | 2533.88 | 2116.68 | 1538.35 | 322.69

## Slide 8
Chart: Age (5 year Groups)
| 0-5 | 6-10 | 11-15 | 16-20 | 21-25 | 26-30 | 31-35 | 36-40 | 41-45 | 46-50 | 51-55 | 56-60 | 61-65 | 66-70 | 71-75 | 81-85 | 86-90 | 91-95 | (blank)
 | 16.5 | 0.46 | 8.14
PCC | 826.01 | 808.52 | 933.75 | 1110.92 | 1228.91 | 890.79 | 656.19 | 318 | 168.78 | 182.48 | 93.4 | 126.71 | 180.83 | 103.31 | 19.84 | 3.91 | 1.34 | 6.75
CRCP | 3.66
HMA over PCC | 2841.83 | 2464.43 | 2707.49 | 1646.99 | 1403.59 | 730.14 | 336.25 | 180.71 | 30.72 | 16.13 | 6.27 | 21.33 | 3.75 | 4.18 | 2.48
HMA | 1158.59 | 425.13 | 662.32 | 286.9 | 377.91 | 367.81 | 194.93 | 54.75 | 0.67 | 29.93 | 24.3 | 48.12 | 14.49
Pavement Inventory
Lane Miles by Surface Type and Age
Notes: Age is the age since resurfacing or age since construction. HMA is hot mix asphalt – and PCC is Portland cement concrete.

## Slide 9
Load (Trucks)
Material
Climate
Construction
Causes of Pavement Distresses

## Slide 10
Load (Trucks)
Fatigue Cracking
Material
Stripping
Climate
Rutting
Construction
Roller marks
Bleeding
Durability Cracking
Oxidation
Blowups
Thermal Cracks
Pot holes (freeze thaw)
Longitudinal Joint
Polishing
Mat Tearing
Segregation
Corner Breaks
Faulting
Rutting
Pavement Distresses and Causes

## Slide 11
Load (Trucks)
Fatigue Cracking
Material
Stripping
Climate
Rutting
Construction
Roller marks
Bleeding
Durability Cracking/Joint deterioration
Oxidation
Blowups
Thermal Cracks
Pot holes (freeze thaw)
Longitudinal Joint
Polishing
Mat Tearing
Segregation
Corner Breaks
Faulting
Rutting
Pavement Distresses and Causes

## Slide 12
Load (Trucks)
Material
Climate
Construction
Pavement Distresses and Causes
Notes: Blow-up in rigid pavement
Thermal cracking in flexible pavement
Erosion of the base leading to punch out in CRC rigid pavement
Potholes every spring

## Slide 13
Load (Trucks)
Fatigue Cracking
Material
Stripping
Climate
Rutting
Construction
Roller marks
Bleeding
Durability Cracking
Oxidation
Blowups
Thermal Cracks
Pot holes (freeze thaw)
Longitudinal Joint
Polishing
Mat Tearing
Segregation
Corner Breaks
Faulting
Rutting
Pavement Distresses and Causes

## Slide 14
Pavement
Notes: The Pavement management strategic plan and the programmatic plan are our guiding documents that shaped the vision for creating the team.
Link investment decisions to this slide – Investing when we are still in the “good” condition
Slowing down the deterioration
Preventive Maintenance/Preservation
  Treatments applied to pavements in relatively good condition to extend pavement life and/or improve performance.
  Begin early in pavement life
  Very cost effective
  Treatments may be repeated on a schedule
  Maintaining Good Condition Costs Less
Just like your car or home, routine and preventative maintenance can help extend the life.
  Eventually things wear out and more extensive rehabilitation or replacement is required.
Over the life of a pavement, preservation treatments are like sealing the deck on your house – it can help extend the life, but eventually it will need rehabilitation or replacement.
We use pavement management data and tools to help us determine the optimal mix of treatments to get the most life at the least cost.

## Slide 15
Pavement
Notes: The Pavement management strategic plan and the programmatic plan are our guiding documents that shaped the vision for creating the team.
Link investment decisions to this slide – Investing when we are still in the “good” condition
Slowing down the deterioration
Preventive Maintenance/Preservation
  Treatments applied to pavements in relatively good condition to extend pavement life and/or improve performance.
  Begin early in pavement life
  Very cost effective
  Treatments may be repeated on a schedule
  Maintaining Good Condition Costs Less
Just like your car or home, routine and preventative maintenance can help extend the life.
  Eventually things wear out and more extensive rehabilitation or replacement is required.
Over the life of a pavement, preservation treatments are like sealing the deck on your house – it can help extend the life, but eventually it will need rehabilitation or replacement.
We use pavement management data and tools to help us determine the optimal mix of treatments to get the most life at the least cost.

## Slide 16
Pavement Treatments
Maintenance and Preventative
$3,000/mile/year of life
  Crack & joint sealing/filling
  Fog Sealing Shoulders
Diamond Grinding
Notes: The treatment costs are in the unit $/mile/year of life. The $/mile refers to the cost of the treatment per lane mile and the “per year of life”
Preventive Maintenance/Preservation
  Treatments applied to pavements in relatively good condition to extend pavement life and/or improve performance.
  Begin early in pavement life
  Very cost effective
  Treatments may be repeated on a schedule

## Slide 17
Pavement Treatments
Maintenance and Preventative
Microsurfacing
$12,000
/mile/year of life
1” Thin Overlay
$5,000 – $9,000/mile/year of life

## Slide 18
Pavement Treatments
Maintenance and Preventative
Microsurfacing
1” Thin Overlay
$5,000 – $9,000/mile/year of life
Diamond Grinding
$9,000/mile/year of life

## Slide 19
Pavement Rehabilitation Treatments
HMA Milling & Resurfacing
Cold In-Place Recycling
PCC Overlay
PCC Rubblization
PCC Crack and Seat
~$40,000/mile/year of life

## Slide 20
Pavement Treatments
Maintenance/Preservation treatments
  Crack & joint sealing/filling
  Diamond grinding
  Thin surface treatments
    Chip seals
    Slurry seals
    Microsurfacing
    Thin lift asphalt overlays
Rehabilitations (20 year life)
  Functional overlays (to address ride)
  Cold-in-Place recycling
  Structural overlays (asphalt and concrete)
  Rubblization/crack & seat
Reconstruction (40 year life)
  Completely replacing the pavement and sometimes the subgrade
$3,000/mile/year of life
$9,000/mile/year
$12,000/mile/year
$40,000/mile/year
$80,000/mile/year
Increasing Annualized Cost
Notes: Costs (from TAMP): Maint/Pres Tx $20k - $50k per lane mile; Rehab Tx $220k - $500k per LM; Recon Tx $600k - $750k per LM

## Slide 21
Interstate Pavement Condition and Future Performance Estimates
Chart: Year
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033
POOR | 0.1 | 0.1 | 0 | 0 | 0.3 | 0.6 | 0.9 | 1.1 | 1.3 | 1.4 | 1.6 | 1.4 | 1.5 | 1 | 1.2 | 0.8
FAIR | 23 | 24.1 | 40.4 | 41 | 39.6 | 41.1 | 44.9 | 43.9 | 39.8 | 39.5 | 38.5 | 36.4 | 35 | 35 | 37.9 | 37.8
GOOD | 76.9 | 75.8 | 59.6 | 59 | 60.1 | 58.3 | 54.2 | 55 | 58.9 | 59.1 | 59.9 | 62.2 | 63.5 | 64 | 60.9 | 61.4

## Slide 22
Non-Interstate Pavement Condition and Future Performance Estimates
Chart: Year
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033
Poor | 2.8 | 2.9 | 3.9 | 3.7 | 3.8 | 4 | 3.8 | 4 | 4 | 4.1 | 4.2 | 3.7 | 3.8 | 3.6 | 3.8 | 4.2
Fair | 49.8 | 50 | 58 | 58.4 | 58.4 | 60.7 | 62.3 | 62 | 62.2 | 61.7 | 63.5 | 63.8 | 63.6 | 62 | 65.2 | 69.5
Good | 47.4 | 47.1 | 38 | 37.9 | 37.8 | 35.3 | 33.9 | 34.1 | 33.8 | 34.2 | 32.3 | 32.4 | 32.5 | 34.4 | 31.1 | 26.3

## Slide 23
Pavement Performance Models
Network Structural Testing
~20% Annually
Friction Data Collection
20% Annually
Pavement Performance Data
Special Investigations Team
Vendor Collected Data
Pavement Modeling

## Slide 24
PCI = 75
PCI = 33
PCI = 50
Notes: PCI stands for pavement condition index. Iowa DOT uses a numerical scale to assess the condition of a roadway’s surface, ranging from 0 to 100 (excellent). It is based on the severity and extent of cracking, roughness, and rutting for HMA) or faulting for PCC. The condition index is used to guide maintenance and repair decisions. Over time, PCI is not generally a steady decline. Cracking in the roadway causes significant increases in roughness and the combination of issues leads to an accelerated decrease in the condition index.

## Slide 25
Non-Interstate Budget Scenarios with Pavement Condition
Chart: Year
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
Status Quo Budget Plus 75% | 73.39 | 72.69 | 72.47 | 72.36 | 72.57 | 72.7 | 72.88 | 73.14 | 74.11 | 74.92 | 75.62 | 76.1 | 76.47 | 76.73
Status Quo Budget Plus 50% | 73.39 | 72.69 | 72.47 | 72.36 | 72.57 | 72.7 | 72.88 | 73.14 | 73.84 | 74.39 | 74.9 | 75.26 | 75.49 | 75.61
Status Quo Budget Plus 25% | 73.39 | 72.69 | 72.47 | 72.36 | 72.57 | 72.7 | 72.88 | 73.14 | 73.56 | 73.86 | 74.15 | 74.35 | 74.45 | 74.47
Status Quo Budget | 73.39 | 72.69 | 72.47 | 72.36 | 72.57 | 72.7 | 72.88 | 73.15 | 73.26 | 73.32 | 73.36 | 73.37 | 73.32 | 73.19
Target | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75 | 75
Notes: Budget scenarios help illustrate how pavement condition will change with time and investment levels.

## Slide 26
Chart: 2035 Investment, $
| 198176782 | 252762805 | 307697952 | 362642129 | 418275190 | 473369851
Investment vs. PCI | 71.79 | 73.19 | 74.47 | 75.61 | 76.73 | 77.82
 | 75
Target | 75 | 75
Non-Interstate Budget Scenarios with Pavement Condition
Target Condition Index
Funding level needed to reach desired condition target

## Slide 27
Interstate Budget Scenarios with Pavement Condition
Target Condition Index
Chart: 2035 Investment, $
| 70007981
 | 80
Interstate Investment vs. PCI | 76.86 | 78.46 | 79.99 | 81.46 | 82.17 | 82.32
Target | 80 | 80
Funding level needed to reach desired condition target

## Slide 28
Historical PCI and Added Life Each Year
Notes: The orange line is pavement condition index over the years. PCI values are shown on the right y-axis. The increase from 2002 to 2007 included transfer of jurisdiction lane miles. In 2012, the pavement condition increased reflecting higher expenditures in years 2009 and 2012-2015. The bar charts show how the pavement life added or reduced from that year’s investment. Life added to the network is predicted for future years based on the status-quo budget. The predicted life is based on an optimized project selection. The year of 2017 saw a low in expenditures resulting. Expenditures were high in 2020. The reduction in purchasing power over time is reflected in the reduced life added shown for future years.

## Slide 29
Project Selection Optimization (Non-Interstate)
Optimization Software Makes Recommendations
Engineers Make Adjustments
Traffic
Field Staff Reviews
Drainage/Safety
Compare and Finalize
Life Added vs Life Lost
Lane Miles Treated
PCI Impact
Notes: We have tools that tell us the most economical way to invest. Engineers take these recommendations and make adjustments based on local feedback and other non-pavement considerations (ie safety). We quantify the impacts of the Engineer’s decisions compared to the optimization tools so we can balance the trade-offs. We make sure we put as much life back as we take out each year through normal deterioration. We make sure our selections offer a similar impact to PCI as the optimization’s recommendations do.

## Slide 30
Pavement Management Key Takeaways
Pavement management team increases our ability to:
  Use models and analytics to direct additional funding
  Enhance strategic project selection
There are competing goals for pavement funding
  Achieve the target 75 PCI condition
  Replace pavements on a reasonable cycle to limit risk of our aging system
Decrease in buying power reduced the ability to add pavement life back to the system.
To achieve pavement performance targets, estimated funding levels needed are:
  $70M for Interstate
  $325M for Non-Interstate

## Slide 31
Questions?